## Slide 1: Documentation images

## Slide 2: Arm Virtual Hardware Targets (VHT)
Precise simulation models of Cortex-M device sub-systems designed for complex software verification and testing
Runs any RTOS or bare metal code
Provides virtual peripheral interfaces for I/O simulation
Enables test automation of diverse software workloads, including unit, integration tests, and fault injection
Cloud service that can be integrated in CI/CD and MLOps development flows
Arm Virtual Hardware Target VHT-Corstone-300
Cortex-M55
TrustZone
Helium
Ethos-U55
microNPU
Memory
Secure/ Non-secure
DMA
Peripherals
GPIO
UART, SPI, I2C
Ethernet
Virtual I/O
Data values
Streaming
BSD-Socket
Debug Interface
MDK, DS
GDB
Event Recorder
Developer Resources
Arm Virtual Hardware Service
I/O drivers
Test scripts
CI/CD integration
Usage examples
Test report tools
Arm VHT Models
C/C++ Compiler
Build utilities

## Slide 3: Virtual Hardware: Test Cloud Applications with Internet Connectivity
Virtual Target
User Application Code (Example)
Virtual Interfaces
Events on changes of LEDs
CMSIS-VIO for Switches/LEDs
CMSIS-RTOS2
FreeRTOS, RTX, …
Python Interface:
- Script for Audio input/output
Ethernet
Demo or test Interface
i.e. Voice Recognition
Application that connects to Internet via BSD-Socket
Audio Driver VSI
Connection to the Internet via Socket
Virtual Streaming Interface (VSI)
Up to 8 VSI instances are supported
Event Recorder Capturing
Virtual Socket Interface (VSocket)
Maps also to a graphical user panel
Demo I/O Interface (VIO)
The interface layer can be re-targeted to physical hardware
Event Recorder
This is a complex user application that requires internet connectivity
Ethernet Driver
TCP/IP Network Stack
VSI is under user control and can service also Video or Sensor data
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 4: Virtual Hardware: Test Cloud Applications with Internet Connectivity
Virtual Target
User Application Code (Example)
Virtual Interfaces
Events on changes of LEDs
CMSIS-VIO for Switches/LEDs
CMSIS-RTOS2
FreeRTOS, RTX, …
Python Interface:
- Script for Audio input/output
Demo or test Interface
i.e. Voice Recognition
Application that connects to Internet via BSD-Socket
Audio Driver VSI
Connection to the Internet via Socket
Virtual Streaming Interface (VSI)
Event Recorder Capturing
Virtual Socket Interface (VSocket)
Maps also to a graphical user panel
Demo I/O Interface (VIO)
The interface layer can be re-targeted to physical hardware
Event Recorder
This is a complex user application that requires internet connectivity
VSI is under user control and can service also Video or Sensor data
BSD-Socket
Socket Driver VSocket
Up to 8 VSI instances are supported
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 5: IoT/ML SW Platform – from FVP to Hardware to Deployment
User Application Code
Ease-of-Use with Open-CMSIS and Keil Studio; provide evidence of correctness on FVP and real deployment
Simulation layer
Stimuli input
SW system under test
Virtual I/O Drivers
Virtual CPU
Event Log file
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 6: FVP Platform for IoT/DSP/ML Software Development
User Application Code
Simulation layer
Events on changes of LEDs
Demo I/O-Driver
CMSIS-RTOS2
FreeRTOS, RTX, …
Python Interface for streaming input
BSD-Socket
Virtual Socket (VSocket)
Demo or test Interface
i.e. Voice Recognition
Event Recorder
Application that connects to Internet via BSD-Socket
Peripheral Driver (e.g., Audio)
Connection to the Internet via Socket
Virtual Streaming Interface (VSI)
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 7: FVP Platform for IoT/DSP/ML Software Development
User Application Code
Simulation layer
Software Under Test (e.g. voice recognition)
Application
Audio Driver
(audio_drv.h/.c)
Virtual Streaming Interface
(arm_vsi.h)
Python Audio streaming Interface
(audio/.../arm_vsi0.py)
Audio files
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 8: FVP/FM Streaming Peripheral Extension
Audio file ‘test.wav’
Cortex-M User Application
First PoC implementation of Streaming Interface
Arm VHT System
i.e. Corstone-300
Virtual Streaming Interface (VSI) Peripheral with Register Interface
Python test script Audio Streaming Interface
Audio I/O Peripheral Driver
Algorithm under Test
In an example we provide the same Audio Peripheral Driver API implemented on a real microcontroller.
The Cortex-M side implements a flexible streaming peripheral that can serve a wide range of use cases. For example, audio I/O.
The streaming peripheral is flexible and allows to implement a wide range of use cases. We show an audio interface in the first example.
Audio files ‘test.wav’

## Slide 9
Code Repository
CI Pipeline
Code update
Start CI
Build
Test
Results
Arm Virtual Hardware
Return CI results
Obtain CI results

## Slide 10: Orta Tools PoC Phase (Audio Use Case)
Reinhard Keil
1. July 2021

## Slide 11: Current Docker Container
https://community.arm.com/developer/tools-software/tools/b/tools-software-ides-blog/posts/infrastructure-for-continuous-integration-tests
Content https://hub.docker.com/r/armswdev/cmsis_tools_m55
  GCC, AC6, FVP Corstone-300 (Cortex-M55), CMSIS pack
Improvement potential
  Better integration to github flows
  Event Recorder for timing measurement
  Ways to specify packs that are outside of the container
  Ways to specify python scripts and simulation data that are outside of the container
  Better examples that show real-world cases
Getting test results to the user
  We need to simplify the way to get useful test results to the user (ideally to the persons that did the commit).

## Slide 12: FVP/FM Streaming Peripheral Extension
Cortex-M User Application
First PoC implementation of Streaming Interface
Corstone-300 Model
Virtual Streaming Interface (VSI) Peripheral with Register Interface
Python test script Audio Streaming Interface
Audio Input Peripheral Driver
Algorithm under Test
In an example we provide the same Audio Peripheral Driver API implemented on a real microcontroller
Also, the Cortex-M side implements a flexible streaming peripheral that can serve a wide range of use cases. Initially we show audio.
The streaming peripheral is flexible and allows to implement a wide range of use cases. We show an audio interface in the first example.
FVP Implementation for Linux and Windows
Audio file ‘test.wav’

## Slide 13: Audio Driver
Data #0
Data #1
Data #2
Data #3
Data #n-1
Block #0
Data #0
Data #1
Data #2
Data #3
Data #n-1
Block #1
Data #0
Data #1
Data #2
Data #3
Data #n-1
Block #2
Data #0
Data #1
Data #2
Data #3
Data #n-1
Block #m
…………
…………
…………
…………
…………
BlockCount
BlockSize
rotating with 2^n blocks
Audio Buffer Handling
Streaming driver for audio data
Support for multiple channels
[support for multiple data formats – after first iteration]
Data transfer in blocks to maximize simulation speed (as it reduces interaction
Callback Event at each block transfer

## Slide 14: Software, Peripheral, and Script interaction
Cortex-M Software
VSI Peripheral
VSI Python Script
Setup Peripheral
Copy Data Block #0
Write registers
Setup Data Transfer
Write DMA registers
Start Operation
Write Timer registers
Timer event
Capture Data Block Size
Capture Register Values
Driver Event (New Data)
Copy Data Block #1
Timer event
Driver Event (New Data)
…
Capture Timer setup
…
Copy Data Block #n
Timer event
Driver Event (New Data)
Stop Operation

## Slide 15: FVP Platform for IoT/DSP/ML Software Development
User Application Code
FVP Layer
Events on changes of LEDs
Demo I/O-Driver
CMSIS-RTOS2
FreeRTOS, RTX, …
Python Interface:
- Script for Audio input
BSD-Socket
Virtual Socket (VSocket)
Demo or test Interface
i.e. Voice Recognition
Event Recorder
Application that connects to Internet via BSD-Socket
Audio Driver
Connection to the Internet via Socket
Virtual Streaming Interface (VSI)
This can is under full user control and can service also Video or Sensor data
Up to 8 VSI instances are supported
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 16: Show & Tell Slides (26. May 2021) Project “Orta” (PoC)
Development process for CI/MLOps with FVP and ArmClang/GCC

## Slide 17: Types of Software Testing
Better quality faster, conforming to safety standards
Unit Testing
  Test little chunks of code at a time.
  Tested against your ‘test’ build.
Integration Testing
  Test whether two components work together when they are combined. Verifies that the interface between them works properly.
  Tested against your ‘test’ build.
System (Black-box) Testing
  Test that final system works as expected. Control external controls & stimuli to system and measure response.
  Tested against your ‘release’ build.
Regression Testing
  Suite of tests (unit & integration tests) & run continuously upon version control updates.
  Used in Continuous Integration (CI)
Orta should make this simpler

## Slide 18: IoT/ML SW Platform – from FVP to Hardware to Deployment
User Application Code
FVP Layer
Simulated I/O via Python scripts and stimuli files
IoT/ML SW Platform
Ease-of-Use with Open-CMSIS and Keil Studio; provide evidence of correctness on FVP and real deployment
Event Log file
User Application Code
Board Layer
IoT/ML SW Platform
Event Log file
Device SDK with configuration
User Application Code
Target Layer
IoT/ML SW Platform
Event Log file
Device SDK with configuration
More Software
More Drivers
FVP Drivers
HW Drivers
Real I/O via test equipment
Real I/O via user peripherals
HW Drivers
Unit & Integration Testing
Deployment (System Testing)
Essential the same event logs are generated across the different deployments. This ensures correctness. Initially: Keil Studio could focus on Ease-of-Use for this process and Event Log Analysis
www.keil.com/mdk5/debug
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 19: IoT/ML SW Platform – for FVP or Real Hardware
User Application Code
FVP Layer
LEDs, Push buttons
Demo I/O-Driver
CMSIS-RTOS2
FreeRTOS, RTX, …
Input stimuli for
Audio, Video, Sensors
Data-Streaming Driver
BSD-Socket
Ethernet-Driver
Demo or test Interface
i.e. Voice Recognition
TCP/IP Stack with Security
Establish a software platform that is foundation for IoT/ML projects.
Cloud Connector C-SDK
Route to internet: enables real communication
Make this part easy to replace with Ethernet, BLE, WiFi, NB-IoT, LoRa, etc.
TF-M provides Security and FOTA services
Event Recorder
Make this part easy to replace to retarget to boards or production hardware
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 20: IoT/ML SW Platform – Usage for Real-world Data Collection
User Application Code
Board Layer
LEDs, Push buttons
Demo I/O-Driver
CMSIS-RTOS2
FreeRTOS, RTX, …
Real-world input
Audio, Video, Sensors
BSD-Socket
Ethernet-Driver
Demo or test Interface
i.e. Voice Recognition
TCP/IP Stack with Security
Event Recorder
Capturing software for real-world data
HW Drivers
Capture real-world input and store in data files
Device SDK with configuration
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 21: FVP/FM Streaming Peripheral Extension
Cortex-M User Application
First PoC implementation of Streaming Interface
CorStone-300 (or Cortex-M4) Model
System C Virtual Streaming Interface (System C Peripheral)
Python Streaming
Interface
Audio Interface
Audio files
Closed Source
Audio Peripheral Driver
Algorithm under Test
In an example we provide the same Audio Peripheral Driver API implemented on a real microcontroller
Also, the Cortex-M side implements a flexible streaming peripheral that can serve a wide range of use cases. Initially we show audio.
The streaming peripheral is flexible and allows to implement a wide range of use cases. We show an audio interface in the first example.
FVP Implementation for Linux and Windows
Test Script

## Slide 22: “Orta” Benefits
For Software Developers:
Verify correctness of software algorithms on Arm target hardware
  FVP represent target CPU accurately which ensures that complex DSP and ML algorithms execute correct
  User benefit: complex input patterns in CI testing are always identical
  Requirement: support for both CI and debug flows (using Keil Studio or established debuggers)
Performance comparison of different algorithms (A/B testing)
  For two different implementations of an algorithm, check which one is more efficient in target hardware.
  User benefit: comparisons with complex input patterns reproduceable; FVP shows no. of instructions (sufficiently precise?)
  Managing user expectations: no real system level simulation, i.e. no cache effects can be identified
  Requirement: time measurement using Event Recorder with Keil Studio (note this is already supported with MDK)
For MLOps Service Providers:
Arm extends reach to deeply embedded systems (more users)
  ORTA workflows simplify the development process (initially for Cortex-M based systems) -> later this should extend to Cortex-A
Arm simplifies ML model deployment with OTA (more services)
  TF-M should scale to mass production and provide usable Update services for ML models
Arm makes it easier to collect real-world data (more compute)
  ORTA enables to collect real-world data
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 23: GitHub Runners and Docker Container
Docker Container with:
Ubuntu latest x86_64 Generic Tools
Python 3.8
curl
wget
bzip2
unzip
git
build-essential (native GCC, make) Arm Tools
Arm Compiler Toolchain 6.15 (Linux x86_64)
GNU Arm Embedded Toolchain: 10-2020-q4-major release (Linux x86_64)
Fixed Virtual Platform model of Corstone-300 MPS2 based platform Cortex-M55 (Linux x86)
Fixed Virtual Platform model of Corstone-300 MPS3 based platform Cortex-M55 + Ethos-U55 (Linux x86) CMSIS Tools
CMSIS Build 0.10.0
PackChk from CMSIS Pack 5.7.0 CMSIS Packs
CMSIS 5.7.0
ARM V2M_MP2_SSE300 Board Support
Can the license entitlement come from a github secret?
Can there be additional packs in github.io?
Is there a way to explain the GitHub actions?

## Slide 24: Run AVT on AMI – from GitHub actions
AMI that runs on EC2 Linux instance
vht.yml defines Run Actions with Input files
Log files
Arm VHT Run Control
*.axf / *.elf Files
Arm VHT System
*.py Python script files
Other Input files (i.e. *.wav)
Via GitHub secrets:
instance_id
access_key
secret_key
vht_in
*.tar file
vht_out
*.tar file
name: 'Run Arm VHT on AMI'
description: 'Run one or more executable files on Arm Virtual Hardware Targets'
inputs:
vht_in:
description: 'input tar file with vht.yml commands, executable images, and input scripts'
required: true
instance_id:
description: 'instance id for connection'
required: true
default: ''
secret_key:
description: 'secret key for connection'
required: true
default: ''
access_key:
description: 'access key for connection'
required: true
default: ''
outputs:
vht_out:
description: 'output tar file with log files from Arm VHT execution'

## Slide 25
Amazon S3 stores data
Step: Execute on Amazon EC2
GitHub
Step: Prepare for execution on Amazon EC2
File vht.yml defines VHT Actions
Executable files (*.axf, *.elf)
Python script files (*.py)
Other input files (*.wav, …)
Output and log files
Execute Build and Test as defined with VHT Actions in vht.yml
VHT AMI image provides tools: VHT Models, Compiler, ...
Source files (*.c, *.cpp, *.h)
Step: Fetch Results from Amazon EC2